## Slide 1: VIDEO BASICS

## Slide 2: Video From Start to till now
Monochrome Video
      Black & White
      Have luminance (brightness) signal and bandwidth
Color TV Video
      3 color
      Increase in bandwidth

## Slide 3: ANALOG VIDEO
NTSC
      Used in North and South America
      30 frames per second with aspect ratio of 720x480
      Each frame is made up of 525 scan lines
PAL
      Use in Asia and other parts
      25 frames per second with aspect ratio of 720x576
      Each frame is made up of 625 scan lines
      Display faster than NTSC
      More information

## Slide 4: ANALOG VIDEO
SECAM
      Developed in France
      625 lines
      25 frames per second

## Slide 5: Interlaced vs Progressive
Interlaced | Progressive
NTSC or PAL or SECAM | Home or office Desktops
Shows odd lines 1st and even lines | Shows in sequential order
Have ghost flickering issue | No ghost flickering issue
Not good for details Less bandwidth compare to Progressive | Suited specifically for details Higher bandwidth

## Slide 6: DIGITAL VIDEO
Audio /Visual in binary format
Easy to store and transfer
Use component video
Advantages over analog
      Direct random access --> good for linear video editing
      Compression
      Transfer

## Slide 7: Analog vs Digital
Analog Signal | Digital Signal
Continuous signal | Discrete signal
Sine wave | Square Wave

## Slide 8: SD vs HD vs 3G
SD | HD | 3G
525 or 625 | 1080i or 720p | 1080p
270 Mb | 1.5 Gb | 3Gb
480i or 576i | 1920x1080 or 1280x720 | 1920x1080

## Slide 9: Video Format
Format = Resolution + Frequency + Frame rate
Resolution = height in pixels X width in pixels
    Eg: 1920 x 1080 for 1080i & 1024x720 for 720 p
Frequency of the video signal
    Eg: 59.94Hz for NTSC and 50Hz for PAL
Frame rate shows the frames per second
    Eg: 59.94i for NTSC and 50p for PAL

## Slide 10: Video Frame
Teletext, close captions, XDS information are send through vertical blanking

## Slide 11: Audio
Analog Audio | Digital Audio
Direct recording | Stream of signal data
Mainly have two audio channels | No limit in audio channel
 | Record while video is recorded
Mono | Stereo | Surrounding
Different Kind

## Slide 12: Types of Audio
PCM
      Product of conversion technique
      Analog to Digital
      Stereo pair audio
Dolby Digital
      Digital audio coding techniques to reduce the data
      Can be any kid mono,stereo, 4 channel, 5.1 channel … etc
      Used to know before as AC-3

## Slide 13: Ancillary Data
AFD ( Active Format Description)
      Sets of code send with video to carry information
      Both in MPEG video streams and Baseband
      Aspect ratio and active picture characteristics are the main information that AFD carry
      Used to generate wide screen signaling (WSS)
WSS (wide screen signaling )
      Digital stream embedded in analog tv signal describing the quality of broadcast ( eg : Aspect ratio of the image)

## Slide 14: Ancillary Data
TeleText
      Created by UK
      Send in vertical blanking internal
      Contain text based information about the video content
Close Captioning
      Process of displaying text on a tv or video screen
      Transcription of the audio portion
      For SD close caption are encoded in to line 21 of vertical blanking interval
      Two standards of close caption CEA-608 used for analog television and CEA-708 closed captions used in digital television

## Slide 15: Ancillary Data
Close Captioning
CEA -608 or EIA -608 | CEA-708 or EIA-708
For analog television | For digital television
Can transmitted on analog and digital television | Only for digital television
Supports up to 2 languages | Support multilingual captions
Transmitted in line 21 | Embedded in MPEG-2 streams
Caption position fixed | Caption position can be changed

## Slide 16: Ancillary Data
VITC ( Vertical Interval Time Code)
      Timing signal part of the video
      Encoded in to vertical blanking interval between successive picture frame or in vertical interval
      VITC assigns time in hour ,minutes and seconds along with frame number
      Used to keep playback machine synchronized with master time source

## Slide 17: Broadcasting